Manufactured or Modular Homes
By Jo Ann Meyer Stratton, IFA, SRA

Many appraisers and home inspectors have a hard time distinguishing manufactured from modular homes- and the differences can be critical. Here's what you need to know.

A manufactured home is constructed in the factory to the national HUD building code and remains a manufactured home forever regardless of how it is installed, what type of foundation and skirting it has or anything else that is done to it. Classification by the local assessing/tax office or other governing agency doesn't change a home constructed to the HUD building code either. 

Typically a manufactured home has a metal frame/chassis/undercarriage that provides structural support for the home after installation. There were a few constructed in the early 1980s that did not have an undercarriage but are still manufactured homes because they were constructed to the HUD building code.

A modular home is constructed in the factory to whatever local building code is applicable for the location it will be installed.  An "off frame” chassis/undercarriage modular home does not have any metal structure to support the home. While under construction in the factory, a steel frame is used as a work table and used to transport the home from the factory to the site, where the home is picked up with a crane and put in place on a prepared foundation. The frame then goes back to the factory for construction of the next "off frame" modular.

An “on frame” chassis/undercarriage modular home has a permanent steel undercarriage/frame/chassis that provides the structural support after the home is installed on site. Both “off frame” and “on frame” modular homes are reported on the 1004 appraisal form.  If it is an “on frame” modular, it will not be eligible for a Fannie Mae loan because of some quirks in their guidelines. Fannie Mae classifies anything with a steel undercarriage as a manufactured home--which would include mobile homes constructed prior to June 15, 1976,  manufactured homes constructed after that date and “on frame” modular homes. The eligibility section of their guidelines state that to be eligible for the mortgage to be purchased by Fannie Mae, the manufactured home has to be constructed to the HUD building code--which eliminates mobile homes and “on frame” modular homes.  If you are appraising an “on frame” modular home, be sure and have the information in the report that it will not be eligible for Fannie Mae. It is eligible for Freddie Mac, FHA and VA. Of course, with the proposed changes at Fannie Mae and Freddie Mac, future regulations are uncertain.

Regardless of what type of factory built home you are appraising or inspecting (or selling), take photos and make notes of all insignias, labels, tags, data plates, etc. that you find on the exterior and in the interior of the home. Include those photos and information in the report.  Appraisers research the tax situation, report what you find  and if the factory built home is not currently taxed as real property, explain what needs to be done prior to close of escrow for it to be taxed in the future as real property.

Remember too that the original building code from the factory while the home was under construction has to be verified prior to completing the appraisal assignment. The original building code is the only answer to whether a home is a manufactured home or a modular home.   Occasionally in some factories, manufactured homes, on frame modular homes and off frame modular homes are all constructed in the same factory, on the same assembly line, with the same floor plan, materials, options, amenities.  Once the construction is complete, someone looking at the homes can not tell which home was constructed to which building code.  

While they were under construction it was constantly being inspected by a state or private inspection agency for compliance to a specific code.   When construction is complete, the inspector will apply HUD labels on the exterior and data plates in the interior for the ones constructed to the HUD building code.  If the home was constructed to a local site built building code like International Residential Code, Uniform Building Code,  Building Officials and Code Administrators, or other similar codes, the state or inspection agency tags/label indicating compliance with that code will be affixed to the home somewhere on the exterior or in the interior or on a framing member in the roofing assembly. Those labels/tags/insignias are the only way to verify the original building code.

Please be sure to support the advertisers who help bring you WRE Online

www.airetesting-design.com

www.homeinspectioninstitute.com

http://www.orep.org/benefits.asp

http://www.mckissock.com/CommonForms/SearchCourses/searchResults.aspx?PartnershipID=%2bP%2b2hF6GqXE%3d